## Slide 1: Group 13 John McFarland Shekh Arefen James Johnson Edgar Velez
Tinjac Is Not Just A Cart
Notes: J-Mac

## Slide 2: Tinjac
Autonomous shopping cart
User inputs shopping list and the cart drives to each item
Automatically calculates the shortest path
Object avoidance
Self tracking

## Slide 3: Motivation
Bringing the future closer to tomorrow
To make shopping easier and a more pleasant experience, especially for older and disabled people
A device able to demonstrate all the skills learned at the University of Central Florida

## Slide 4: Goals and Objectives
Saving customers time and money
A device accessible for people of all types of different walking speeds
Low technological cost
Develop a prototype that can be easily adopted
End product will have no exposed wires
Environmentally friendly power source
Cart be able to accurately know the location of the items in the store

## Slide 5: Block Diagram

## Slide 8: Core Features
Easy to use UI with the ability to add and subtract items from the shopping list even after the cart is in motion
The shopping cart has an accurate map of the store it’s in
The shopping cart is able to avoid obstacles using infrared sensors and sonar modules to adjust the speed of the cart
If the user stops walking, the cart will also stop accordingly
Rechargeable 12V power supply with a solar panel
Total cart weight is around 15 lbs
Cart should be able to hold at least 50 lbs
Dimensions are 21 by 24.5 inches, smaller than a regular cart

## Slide 11: MSP-430F5529LP
Simplicity
Ease in configuring GPIO pins
3.3V
Notes: J-Mac End

## Slide 12: 12V DC Motor 146 RPM w/Encoder
Met the requirements we initially set:
Move the cart given that it can carry a certain amount of weight.
Speed of the cart should be about the same as the average walking speed of a person.
Notes: Eddy G

## Slide 13: Gowoops E18-D80NK
Is used for obstacle detection and to see if the user is still following the cart
Ultimately chosen because it had the highest detection distance range (80 cm)
3.3V-5V

## Slide 14: HC-SR04 Ultrasonic Sonar Module
Used for obstacle detection with a range of 400 cm
Has low power consumption so the battery can last longer
5V

## Slide 15: RioRand 20x4 LCD Module
LCD display has 4 lines with 20 characters each
Will mainly be used for inputting the shopping list
Can also be used to to display error messages
5V

## Slide 16: EXP1270 Rechargeable Lead Acid Battery
12 Volt, 7 amp rechargeable battery
Dimension: 5.9 x 2.5 x 3.7 inches
Weight: 4.3 lbs

## Slide 17: EcoWorthy Solar Panel
Water and dust proof to protect against rough weather
Corrosion resistant aluminum frame for extended outdoor use

## Slide 18: Anself Solar Charge Controller
Prevents over-loading and short-circuiting
Prevents the battery from over-charging
12-24V range, 10 A

## Slide 19: LMZ12002 Voltage Regulator
Up to 2-A Output Current.
Input Voltage Range 4.5 V to 20 V
Output Voltage Range 0.8 V to 6 V

## Slide 20: TPS563210ddf Voltage Regulator
Up to 3-A Output Current.
Output Voltage Range 11.5 V to 3.3 V

## Slide 21: Goplus Double Basket Folding Shopping Cart
Provides additional basket, allowing more flexibility when installing our hardware components
Weighs only 13 lbs with a holding capacity of 120 lbs
Has swivel wheels, allowing the cart to travel backwards without having to worry about the front wheels
Notes: Eddy G End (Endy G)

## Slide 22: Overall Schematic
Notes: Jimmy Start

## Slide 23: Printed Circuit Board (PCB)

## Slide 24: Software Design
Core Function List:
User Interface
Create Path
Run Cart
Obstacle Detection
Movement Correction
Secondary Function List:
Shopper Check
Pause Cart
Hard Reset
Emergency Stop

## Slide 25: User Interface Function
Takes in user input from the different buttons that will communicate with the microcontroller
User will be able to select their grocery items and the program will proceed to the Create Path Function
Will also be able to communicate warnings/status updates with the customer

## Slide 26: Create Path Function
Takes in the selected items, calculates the shortest path, and is passed on to the Run Cart function
References a predetermined layout of the store, with entrance and checkout locations
Will implement a modified version of Dijkstra’s algorithm to find the optimal path

## Slide 27: Run Cart Function
When this function is called, shopping cart moves forward while checking for any obstacles or potential collisions.
Checkpoints will be set up so that the shopper can either wait after getting an item or continue on
Once the journey is finished, the cart will head back to the starting point

## Slide 28: Obstacle Detection
Will check for any potential obstacles or collisions
Works in combination with both the sonar and IR modules
When an object is detected in the path of the cart, the Movement Correction function will be called

## Slide 29: Movement Correction
Once an obstacle is detected, the location of that obstacle in relation to the cart’s path will be recorded
Depending on where the obstacle lays, the cart will be triggered to move around the obstacle
The function will then calculate how much further from the original path the cart has travelled.

## Slide 30: Final Software Implementation
Notes: Eddy G Peaces again

## Slide 31: Secondary Functions
Shopper Check
Detects when the shopper is too far away from the cart.
If they are, the cart stops, and waits for the shopper to return.
Pause Cart
Pauses the cart and waits for the customer to hit the button to continue.
Important for safety.
Hard Reset
Shuts down everything that Tinjac is doing, generally when errors occur.
New path generated with current location as starting point.
Emergency Stop
Serves as an emergency fail-safe.
Activated if there is a physical issue that can no longer be resolved with software.
All power is cut off except for the user interface.

## Slide 32: Demonstration Test
Notes: James n his Gamez

## Slide 33: Work Division
 | Power | Motors | Sensors | UI
Edgar | Primary | Secondary |  | 
James | Secondary | Primary |  | 
John |  |  | Primary | Secondary
Shekh |  |  | Secondary | Primary

## Slide 34
Item Name | Quantity | Price/Part | Cost/Order
High-Torque Motor | 2 | ≈ $45 | $90
MSP 430 | 2 | ≈ $3.66 | $7.32
Compact Size Shopping Cart | 1 | ≈ $50 | $50
Solar Panel | 4 | ≈ $10 | $40
High-Capacity Rechargeable Battery | 1 | ≈ $20 | $20
Sonar Module | 2 | ≈ $4 | $8
Infrared Module | 9 | ≈ $9 | $81
L293D Motor Driver Chip | 1 | ≈ $1 | $1
Miscellaneous Wires/Gears | N/A | ≤ $10 | $10
PCB board | 10 | ≈$15 | $15
PCB parts | N/A | ≈$10 | $10
LCD Module | 1 | ≈ $10 | $10
Total: |  |  | $342.32
Budget

## Slide 35: Challenges
Combining our UI code to cooperate with our sonar sensor code
PCB was printed wrong due to manufacturer
Deciding which MCU to use
Mechanical design of cart

## Slide 36: End Result/Demo
See main page of website

## Slide 37: Stretch Goals
An app that replaces the physical user interface
Using a button or app to call a shopping cart to your location
Alternate cart mode that follows the shopper
An item scanner on the cart
Cart can hold 100 pounds
Cart should be able to follow the shopper to their car

## Slide 38: Experience Gained
Effective Collaboration/Communication
Technical writing skills
Time management
Real life setup of circuits and components
Integration of hardware + software
Notes: Jimmy Finale

## Slide 39: Questions?