## Slide 1: Home Safety and Automation System
Group 14
Felix Henriquez, CPE
Guilherme Costa, CPE
Matthew Allen, CPE
Avery Stevenson, PSE

## Slide 2: Executive Summary
The main objective of our project is to create a modular and simple to use Home Safety and Automation System that can be easily installed and maintained by anyone in their household.

## Slide 3: Motivation
Cost Effective Home Automation
More Secure Data Management
Manage Home Energy Efficiency
Seamless Installation with Modular Components
Reliability
User Friendly Configurable UI

## Slide 4: Sensors and Accessories
Motion Sensors
Fire Detectors
Fire Detector Housing and Baseplate
Lens

## Slide 5: Fire Detection Unit
Specification | Value
Input Voltage | 5V
'On' Output Voltage | 0V
'Off' Output Voltage | 5V
Steady State Current | 90uA
Range | 2 Feet
Steady State Power Consumption | 450uW
Angle of Detection | 60 Degrees
Optical Bandwidth | 0.7-1.1um
NIR photodiode
LM2596 step-down voltage regulator with 9V battery
Potentiometer adjustment
NIR Photodiode

## Slide 6: Fire Detection Limitations
Cannot be in direct sunlight
Cannot be directly in lighting
Detects objects over 250F
Fluorescent Lamp Spectrum
Typical Fire Emission Spectrum

## Slide 7: Fire Detector Housing
N-BK7 plano-convex lens
1” focal length
Acrylic baseplate and housing
Housing Dimensions: 1.4”x 2.5”x 1.5”
N-BK7 Lens
Sensor Housing and Baseplate
N-BK7 Transmission Spectrum

## Slide 8: Motion Sensor Module
Specification | Value
Range | 5m
Angle of Detection | 120 Degrees
Input Voltage | 9V
'Off' Output Voltage | 3.32V
'On' Output Voltage | 40mV
Steady-State Current | 5mA
Steady-State Power Consumption | 16.5mW
PIR sensors
Fresnel lenses
Potentiometer Adjustment
PIR Sensor

## Slide 9: Motion Sensor Limitations
Only Detects Motion
Positive and Negative Polarized Detection Areas
Motion Detection Diagram
Motion Sensing Photodiode

## Slide 10: Home Automation Devices
Design Overview
Standard Sizes
Standard Current and Voltage Compliance
Meets NEC Standards
Functional Regardless of Connection

## Slide 11: Product Requirements
Specification | Requirement
Outlet/Switch Minimum Max Current | 15A
Outlet/Switch PCB Max Dimensions | <3”x2”x2”
Wireless Range | 30M
AC Thermostat input/Output | 24VAC
Display Room Temp (AC) | <5% error
Wire Size | 12AWG

## Slide 12: Smart Outlet
Components Needed
Boost Converter
AC-DC 3V3
20 Amp Relay
Current Limiting Resistor
Optocoupler
Current Sensor
WiFi MCU
Config Button
Frame
Outlet
Xl6009 Step-Up Converter
AC-DC Power Module
ACS Hall Effect Sensor
Relay
Relay Driver Circuit
ESP-12f

## Slide 13
Outlet Schematic

## Slide 14
PCB Layout of Components

## Slide 15
Name | Designator | Footprint | Quantity | Manufacturer Part | Manufctr | Price
XL6009 | U1 | XL6009 | 1 | XL6009 | LC Tech | $ 1.60
HLK-PM01 | U2 | PWRM-TH_HLK-PM01 | 1 | HLK-PM01 | HI-LINK | $ 2.50
4N35 | U3 | DIP-6 | 1 | 4N35 | EVERLIGHT | $ 0.10
SRA-12VDC-CL | K1 | SRA-12VDC-CL | 1 | SRA-12VDC-CL | SONGLE | $ 0.25
1k | R1 | AXIAL-0.3 | 1 | Generic | Generic | $ 0.01
ACS712 | U7 | ACS712 MODULE REV01 | 1 | ACS712 | LC Tech | $ 1.24
ESP-01S | U4 | ESP-01S | 1 | ESP-01S | Ai-Thinker | $ 1.22
40mm x 60mm PCB | PCB | PCB | 2 | Generic | Generic | $ 0.44
Dual Receptacle | SW | None | 1 | Switch SPDT | Levington | $ 1.60
Surface Mount Box | HS | None | 1 | Box Mount | Levington | $ 5.99
Switch Frame | SF | None | 1 | Frame | Generic | $ 1.00
 |  |  |  |  | Total | $15.95
BOM Smart Outlet

## Slide 16: Smart Switch
Components Needed
Boost Converter
AC-DC 3V3
Relay
Current Limiting Resistor
Optocoupler
Current Sensor
WiFi MCU
Config Button
Frame
3-Way Switch

## Slide 17
Switch Schematic

## Slide 18
PCB Layout of Components

## Slide 19
Name | Designator | Footprint | Quant | Manufacturer Part | Manufacturer | Price
XL6009 | U1 | XL6009 | 1 | XL6009 | LC Technologies | $ 1.60
HLK-PM01 | U2 | PWRM-TH_HLK-PM01 | 1 | HLK-PM01 | HI-LINK | $ 2.50
4N35 | U3 | DIP-6 | 1 | 4N35 | EVERLIGHT | $ 0.10
SRA-12VDC-CL | K1 | SRA-12VDC-CL | 1 | SRA-12VDC-CL | SONGLE | $ 0.25
1k Resistor | R1 | AXIAL-0.3 | 1 | Generic | Generic | $ 0.01
ACS712 | U7 | ACS712 MODULE REV01 | 1 | ACS712 | LC Technologies | $ 1.24
ESP01S | U4 | ESP-01S | 1 | ESP-01S | Ai-Thinker | $ 1.22
40mm x 60mm PCB | PCB | PCB | 2 | Generic | Generic | $ 0 .44
3-Way Paddle Switch | SW | None | 1 | Switch SPDT | Levington | $ 5.82
Surface Mount Box | HS | None | 1 | Box Mount | Levington | $ 5.99
Switch Frame | SF | None | 1 | Frame | Generic | $ 1.00
 |  |  |  |  | Total | $20.17
BOM Smart Switch

## Slide 20: Smart Thermostat
Components Needed
4x Relay Circuit
ESP-12F
Stepdown Converter
Diode
Capacitor
Temp and Humidity Sensor DHT21
12AWG Connector Headers
I2C Display
Config Buttons
Multiplexer
Acrylic Housing
DHT21 Temp Sensor
1.8" OLED Display
AC Relay Circuit

## Slide 21
Thermostat Schematic

## Slide 22
PCB Layout of Components

## Slide 23
Name | Designator | Footprint | Quantity | Manufacturer | Price
ESP8266 Relay Module | X4 | Custom PCB | 1 | LC Technologies | $ 5.50
NodeMcu ESP8266 V3 CH340 (Version 1.0) | U1 | NEW PCB NODEMCUV3 | 1 |  | $ 2.14
LM2596 Module | U2 | LM2596 DC-DC BUCK CONVERTER ADJUSTABLE POWER SUPPLY STEP DOWN MODULE | 1 |  | $ 0.99
1N4448 | D1 | DO-35 | 1 | SEMTECH | $ 0.10
1u | C1 | CAP-D3.0XF1.5 | 1 |  | $ 0.10
DHT22 | U3 | DHT22_AM2303_HORIZ | 1 |  | $ 2.69
Header-Female-2.54_1x5 | H2 | HDR-5X1/2.54 | 1 | BOOMELE | $ 0.15
WJ2EDGVC-5.08-3P | P1 | WJ2EDGVC-5.08-3P | 1 | ReliaPro | $ 0.12
OLED_Display_I2C PM | P2 | 0.96 AND 1.3 I2C OLED SSD1306 | 1 |  | $ 1.76
CD74HC4052M96 | U4 | SOIC-16_150MIL | 1 | TI | $ 0.25
Acrylic Housing | HO | NONE | 1 | Generic | $ 5.00
 |  |  |  | Total | $18.80
BOM Smart Thermostat

## Slide 24: Flame And Motion Detectors
Components Needed
Battery
Step-down Converter
Step-up Converter
ESP-12F
Detector
Battery Connector
Housing
Lens

## Slide 25
Flame Detector and Motion Sensor Circuit Schematic

## Slide 26
PCB Layout of Components

## Slide 27
Name | Footprint | Quantity | Manufacturer Part | Manufacturer | Price
9_Volt Battery | BH9VW | 1 | No.7 | ReliaPro | $1.00
LM2596 | STEP_DOWN_LM2596S | 2 | LM2596 | LC Technologies | $1.40
FLAME-DETECTOR | FLAME-DETECTOR | 1 | LM393 | LC Technologies | $0.50
ESP01S | ESP01S | 1 | ESP8266-01s | Zuc Zuc | $1.67
Battery Connector | N/A | 1 |  | Generic | $0.25
Housing | N/A | 1 |  | 3D Print | $5.00
Lens | N/A | 1 |  |  | $10.00
 |  |  |  |  | 19.82
BOM Detectors

## Slide 28: Component Software Design
Key Features
MQTT Machine-2-Machine Communication between System Controller and Device.
Works by Publishing or Subscribing to data streams.
Either Sends Data or responds to commands, Does not need to perform calculations.
Only 512KB of available memory.
Connects directly to System Hub
Using Arduino IDE C++ Scripting

## Slide 29: Classes
Main Setup Loop Reset | Connection Setup HubConnect | Communications Setup Publish Subscribe Listen Respond
RelayControl (Outlet/Switch) Setup Trigger | SensorControl Setup ReadData | AC Control (Thermostat) Setup SetTemp ReadTemp ProcessChanges

## Slide 30: System Diagram
Needs to be re-done

## Slide 31: Back-end and Front-end Design

## Slide 32: Requirements Specifications
Component | Parameter | Requirement
Security | Security of System | System will prevent unauthorized access attempts
Capacity | Minimum Users | System should be able to support a minimum of 10 user accounts
Stability | Control of System | Up to 5 concurrent users logged in
Interface | Ease to Use | GUI is intuitive and unobtrusive
Home Safety and Automation System – Group 14

## Slide 33: Back-end Framework
Allows for rapid deployment
Written in Python
Great documentation
Many extra modules available
Versatile features

## Slide 34: Database Selection
Feature | MySQL | MongoDB
Easy Integration |  | 
Organization | Tie | Tie
Support |  | 
Documentation |  | 
Load Handling |  | 

## Slide 35: Cloud Computing Service
Service | Cost ($) | Top Feature(s)
Amazon Web Services | 15 | Variety of Services
Digital Ocean | 5 | Cost Effective and Freedom
Heroku | Free | Cost
Amazon Web Services
Digital Ocean
Features in Use
Simple Storage Service (S3)
Simple Email Service
WorkMail
Features in Use
Droplet
Domain Handling

## Slide 36: Front-end Design
Material Design Bootstrap
Choices:
Plain HTML/CSS
Bootstrap
Material Design Bootstrap
Materialize CSS

## Slide 37: User Registration Example
When creating a local account the user should fill out a similar form
Home Safety and Automation System – Group 14

## Slide 38: View and Edit Profile
The User will also have the option to view and edit their profile information
Home Safety and Automation System – Group 14

## Slide 39: Dashboard
Home Safety and Automation System – Group 14

## Slide 40: Dashboard – Adding Device
Home Safety and Automation System – Group 14

## Slide 41: Dashboard – Tasks
Home Safety and Automation System – Group 14

## Slide 42: System Hub Design

## Slide 43: System Hub
Raspberry Pi 3 Model B+ with Raspbian operating system chosen to serve as the system hub.
Provides robust suite of hardware including Wi-Fi and Bluetooth connectivity, can interface directly with other components via USB, HDMI, GPIO pins, etc.
Serves to connect smaller, simpler components of the system spread throughout the house with the online management system proper.
Component | Specification
CPU | Broadcom BCM2836B0 Cortex-A53 (ARMv8) 64-bit SoC @ 1.4 GHz
Memory | 1GB LPDDR2 SDRAM
Wireless Networking | 2.4GHz and 5GHz IEE 802.11.b/g/n/ac wireless LAN, Bluetooth 4.2, BLE
Wired Networking | Gigabit Ethernet over USB2.0 (maximum throughput 300 Mbps)
Pin I/O | Extended 40-pin GPIO header
USB | 4 USB 2.0 Ports
Digital Video | Full-size HDMI
Analog AV | 4-pole stereo output and composite video port
Storage | Micro SD port
Power | 5V/2.5A DC Power input

## Slide 44: Networking Overview
Client-Server Communication
  Use webservice-based communication as a means of simplifying data interchange between client and server.
  Use Django REST framework to facilitate creation of REST API.
  Connect to internet via user's local area network, either via wired connection or Wi-Fi.
Hub-Device communication
  Long-distance communication carried out via Wi-Fi-direct connection between hub and Wi-Fi capable devices.
  Short-range communication can be carried out via more direct means if devices are positioned near hub, via GPIO pins, etc.

## Slide 45: Networking Cont'd.
User should not be required to perform networking configuration in order to get system working.
Design client-server networking such that port forwarding will not be necessary.
  Query server for updates of device information stored in database
  Send information on changes observed on the client-side to the server.

## Slide 46: JSON Data
Information about the state of supported devices will be transmitted and received in JSON format, as JSON is the format of choice for REST based web service frameworks.
Generalized object format for devices in general which includes device ID and device type, with nested device-specific JSON object which contains information related to the device in question.
I.E. 'wire' status and target temperatures for thermostat tie-in device, on/off state for lightbulbs and power consumption readings for smart outlets, etc.
Example: Chart of fields for a smart outlet internal JSON object:
Field | Data Type
Toggle Status | Boolean
Current (is present) | Boolean
Current (consumption) | Integer

## Slide 47: MQTT topic hierarchy
Topics separated by device-type and placed under an all-encompassing 'devices' parent topic.
  Examples:
  Devices/HVAC_control
  Devices/Sensors_control
Allows for reduction of clutter in messages which the modules are expected to interpret while allowing the hub to listen in on all communications via the "devices/#" multi-level wildcard string.

## Slide 48: Administrative Content

## Slide 49: Division of Work
System Component | Primary | Secondary
Sensors | Avery | Felix
Embedded Systems | Felix | Avery
Back-End | Costa | Matthew
Database | Costa | -
API | Costa | -
Communication | Matthew | -
Front-End | Matthew | Costa

## Slide 50: Milestones
Milestone | Deadline | Status
Parts Ordered | September 1st | Completed
Sensor Testing | September 30th | In Progress
Communication Testing | September 30th | Planned
Initial Coding | October 6th | In Progress
Initial Prototyping | October 13th | Planned

## Slide 51: Budget
Component | Price ($)
Thermostat | 35
Outlet | 30
Switch | 30
Sensors | 20
Lens | 40
System Controller | 40
Web Services | 30
Total | 225
Planned | < 250

## Slide 52: Project Progress
Chart: 
| Research | Design | Prototyping | Coding | Testing | Parts Acquired
Progress | 0.95 | 0.85 | 0.1 | 0.45 | 0.65 | 0.9

## Slide 53: Questions?