## Slide 1: Beam
Group 1
TJ Jones
Ryan Takiff
Suhyun Hwang
Daemy Luzardo
Botanical eradication and management machine

## Slide 2: Meet the Team!
Ryan Takiff
Electrical Engineering
Suhyun Hwang
Photonic Science
Engineering
TJ Jones
Electrical Engineering
Daemy Luzardo
Electrical Engineering

## Slide 3: Motivation & Background
Why is weed control important?
Weeds compete with crops for essential nutrients in the soil
They absorb water from the soil
Weeds can overshadow crops, blocking sunlight that is necessary for photosynthesis
Many weeds serve as hosts for insect pests and other organisms that can harm crops

## Slide 4: Motivation & Background
Use more cost-effective materials and components
Develop an echo-friendly method : evaporating the weeds (avoiding burning or spraying)
Mobile app integration for remote monitoring and control

## Slide 5: Goals and Objectives
The main objective of our project was to build a robot capable of navigating a field or farmland.
Then the robot uses a guided laser system to remove unwanted weeds.
Providing farmers with a more environmentally friendly weed control method
Ryan, EE

## Slide 6: Robot Specific Objectives
Robot should be able to use the solar panels to charge its own batteries while out and operating.
Robot should be capable of basic autonomous navigation without getting stuck or lost.
Create a simple application to keep track of weed data as well as other important trackers.
Ryan, EE

## Slide 7: Laser System Objectives
Design a lightweight and compact laser control system for the robot, allowing for greater portability.
Achieve a high-power output from the laser diode, ensuring efficient moisture evaporation.
Integrate proper safety features to ensure safe operation around humans and other fragile objects.
Ryan, EE

## Slide 8: Advanced Goals
Add a sufficient cooling system for all the electronics on board.
Create a 3D actively updated map model of the where the robot is along with its surroundings
Using SLAM localization for improved route planning, and greater adaptibility
Ryan, EE

## Slide 9: Stretch Goals
Make the robot highly water resistant and create proper housing for each component and modify the chassis so that water does not penetrate the robot’s infrastructure
Application for the robot would let users monitor the progress of weed removal in their field and document weed location so the user would know where problem areas are located.
Use Slam Localization to fully automate all of the robot's functionality
Ryan, EE

## Slide 10: BEAM Description

## Slide 11: Laser Control System

## Slide 12: Engineering Specifications
Chassis | 
Length x width x height | 1.6ft x 1.6ft x 1.25ft
Weight | ~60 lbs.
Material | Aluminum
Solar Panel | 
Maximum Power | 6 W
Maximum Voltage | 15 V
Battery | 
Maximum Lifespan | 10 h
Maximum Voltage | 12.8 V

## Slide 13: Engineering Specifications Cont.
Laser Source | 
Wavelength Range | 450 – 550 nm
Optical Power | 1000 – 5500 mW
Laser System | 
Location accuracy | ≤ 1 cm
Weed Treatment | 
Treatment Time | 20 – 30 seconds
Treatment Distance (Laser Pointer End to Plant) | 5 – 10 cm
Weed Identification Efficiency | Expected at 70-85%

## Slide 14: Hardware Comparison and Selection

## Slide 15
Hardware Block Diagram
IDE
TJ, EE

## Slide 16: Battery Selection Lithium vs. Lead-acid
Specs | LiFePO4 | Lead-Acid | Notes
Specific Energy (Watt Hours/kg) | 150-250 | 30-50 | LiFePO4 is lighter and packs more energy
Charge Time | 2-4 hrs | 8-16 hrs | LiFePO4 has quicker charge times
Cost (per kWh) | $100-300 | $150-200 | LiFePO4 tends to range higher than lead-acid, but some manufacturers offer similar prices
TJ, EE

## Slide 17: Solar Panel Selection Monocrystalline vs Polycrystalline
Specs | Monocrystal | Polycrystal | Notes
Efficiency | ≥ 23% | ≤ 20% | Increased efficiency for monocrystal
Cost per Watt | $1-1.50 | $0.90-1.50 | Monocrystal tends to lean more expensive than polycrystal
*Temperature Performance | 0.38 - 0.44% | 0.44 - 0.50% | Increased performance in outdoor temperatures for monocrystal
TJ, EE
*Lower Temperature performance is better!

## Slide 18: Charge Controller Selection Main functions: - Supply adequate voltage for battery charging - Regulate charging current - Prevent battery overcharge
Specs | MPPT | PWM | Notes
Voltage Compatibility | Wide range of voltages | Fixed voltage | MPPT offers more precise voltage control for LiFePO4 batteries than PWM
Efficiency | 95-99% | 70-85% | MPPT offers more power efficiency
Cost | $25-40 | $12-30 | While MPPT is typically more expensive, they also offer better efficiency and precision
TJ, EE

## Slide 19: Charge Controller Selection
Specs | Ratings
Voltage Input | 15 to 30V
Current Output | 10A
Weight | 0.32lbs
Cost | $36.99
Specs | Ratings
Voltage Input | ≤ 30V
Current Output | 10A
Weight | 0.375lbs
Cost | $39.99
Bateria Powers' MPPT Solar Charge Controller
Voltset's MPPT Solar Charge Controller
TJ, EE

## Slide 20: Charge Controller Selection
Specs | Ratings
Voltage Input | 15 to 30V
Current Output | 10A
Weight | 0.32lbs
Cost | $36.99
Bateria Powers' MPPT Solar Charge Controller
TJ, EE

## Slide 21: Voltage Regulator Selection: Switching Regulators vs Linear Regulators Main function: Step down 12V to 5V/3.3V for powering electronics
Specs | Switching Regulator | Linear Regulator | Notes
Load Efficiency | 65-80% | 15-20% | Increased efficiency reduces power loss and heat generated
Circuit Design Complexity | 6-11 Components | 3-5 Components | Switching regulator is more complex, yet needs less board space due to less power loss
Cost | $5-15 | $2-5 | Switching regulator has increased cost and more components, but better performance
TJ, EE

## Slide 22: Switching Regulator Selection
Specs | Ratings | Notes
Voltage Input | 4.5 to 52 V | Sufficient
Voltage Output | 0.7 to (Vin-10V) | Sufficient
Max Current Out | 3A | Sufficient
Power Efficiency | ≤ 94% | Higher efficiency
Specs | Ratings | Notes
Voltage Input | 3 to 40 V | Sufficient
Voltage Output | 1.25 to 40V | Sufficient
Max Current Out | 1.5A | Less than required Iout
Power Efficiency | ≤ 87.7% | Slightly lower efficiency
Texas Instrument's TSP40200
Texas Instrument's MC34063ADR
TJ, EE

## Slide 23: MCU Selection Main functions: - Decision making - Manage and execute multiple tasks - Collect, process, and transmit data between devices
Specs | ESP32WROOM | Arduino LoRA | Notes
Microcontroller | Dual-core 240 MHZ | ARM Cortex M0+ | ESP has higher performance and computational capacity
Clock speed | 240 MHZ | 48 MHz | ESP clock speed is 5 times faster
Flash Memory | 4 MB | 256 KB | ESP has over 3MB more space
GPIO Pins | 34 | 22 | ESP has more GPIO pins, which are essential for BEAM
Analog Inputs | 18 | 7 | ESP more than doubles inputs
Ryan, EE
Specs | ESP32-WROOM | Arduino LoRa | Notes
Microcontroller | Dual-core 240 MHz | ARM Cortex M0+ | ESP has higher performance and computational capacity
Clock speed | 240 MHz | 48 MHz | ESP clock speed is 5 times faster
Flash Memory | 4 MB | 256 KB | ESP has over 3MB more space
GPIO Pins | 34 | 22 | ESP has more GPIO pins, which are essential for BEAM
Analog Inputs | 18 | 7 | ESP more than doubles analog inputs
Price | ~$4.34 USD | ~$35-40 USD | ESP is more cost-efficient for most IoT projects
Size | 18mm x 25.5mm | 25mm x 45mm | ESP is more compact
Manufacturer | Espressif Systems | Arduino (LoRa by Semtech) | 

## Slide 24: Raspberry Pi 4B Main functions: - Object recognition - Board to board communication protocols (I2C, UART, WiFi) - parallel processing real-time data
Ryan, EE
Feature | Arduino MKR WAN 1300 | Franzininho Board | Raspberry Pi 4 Model B
Microcontroller | ARM Cortex-M0+ | ATtiny84 | Broadcom BCM2711 (Quad-core Cortex-A72)
Clock Speed | 48 MHz | 20 MHz | 1.5 GHz
Flash Memory | 256 KB | 8 KB | microSD (Expandable)
SRAM | 32 KB | 512 B | 2/4/8 GB LPDDR4
GPIO Pins | 22 | 12 | 40
Analog Inputs | 7 | 8 | -
Digital I/O Pins | 22 | 12 | 40
WiFi | No (LoRa connectivity) | No | Yes
Price | ~$39 USD | ~$10-15 USD | ~$35-55 USD
Size | 2.7" x 1" (68.6mm x 25.4mm) | 29mm x 13mm | 85.6mm x 56.5mm
Manufacturer | Arduino | Franzininho Project | Raspberry Pi Foundation
Notes for BEAM | Good for low-power wireless communication | Compact but lacks advanced features | High computational power for BEAM Requirements

## Slide 25: Motor Type Selection
Specs | Brushed DC Motor | Stepper Motor | Notes
Torque | High | Low | The selected Torque for stepper motors must be precise.
Motor Speed Control | PWM | Counts number of steps | DC motors have a simple speed motor control, but SM are more precise
Maintenance | High | Low | DC motor brushes wear over time
Cost | $10-50 | $15-100 | Dc Motors have lower initial cost
Daemy, EE

## Slide 26: DC Motor Selection Main functions: - Powering the robot's wheels - Traversing rough terrain
Specs | RS550 | Mabuchi 555SH | Notes
Operating Voltage | 5-15 V | 12V | Both can operate within a range but 12V was chosen
Rated Torque | 265 g.cm | 420 g.cm | Torque can be improved with a gear box
Rated Current | ≤2A | 1.5A | Can vary depending on the speed and runtime
Speed | 4000 RPM | 5100 RPM | Speed was not the main concern
Weight | 150 g | 200 g | Less weight helps with speed
Cost | $16-20 | $18-25 | The difference wasn’t significant
Daemy, EE

## Slide 27: Transmission and Tire Selection
Speed upgraded to 40000 RPM.
Gearbox composed of three gears; the middle one is metal.
All terrain wheels were chosen to navigate outdoors.
Wheels’ materials are rubber and plastic.
8-inch diameter.
Daemy, EE

## Slide 28: Motor Driver Selection Main functions: - Powering the DC motors
Specs | BTS 7960B | TB67H420FTG | Notes
Supply Voltage limit | 45 V | 50 V | Has no impact to selection due to high limit
Quantity needed for navigation | 8 | 2 | Corresponds to bidirectional functionality
Size | 9.9mm x 14.9 mm | 7mm x 7mm | Bigger dimensions help with soldering
Path Resistance | 18 mΩ | 0.33Ω | A lower path resistance is wanted
Current limit | 43A | 9A | Higher current limitation is wanted to prevent damaged to IC
Price | ~1 | ~$5 | The total price for the BTS7960B would be lower despite the difference in quantity
Daemy, EE

## Slide 29
Hardware Block Diagram
Peripheral Components
Peripheral Components
IDE
TJ, EE

## Slide 30: Peripheral Components
LIDAR​
​
Robot navigation and obstacle detection​
Communicates distance data with ESP32 for obstacle detection and area recognition
Raspberry Pi 4 Camera
An RGB camera that sends image data to Raspberry Pi for weed detection and location
Linear Actuator​
Uses a 12v DC motor to lower safety shutter for laser protection
TJ, EE

## Slide 31: Sensor Selection: Sonar vs Lidar Main function: Robot navigation and obstacle detection
Specs | Lidar | Sonar
Detection Medium | Light | Sound
Range | Can be up to 200m | Can be up to 50m
Accuracy | mm range | cm range
Speed | Faster data acquisition | Slower data acquisition
Environment | Sensitive to weather conditions | Works well in low visibility
Applications | 3D Mapping/Autonomous vehicles | Object detection and depth sensing
TJ, EE

## Slide 32: RPLIDAR A1 by SLAMTECH
360-degree scan with 12-meter range
Produces 2D point cloud data that can be used in mapping, modeling, and localization
Can function well in indoor and outdoor settings and without direct sunlight exposure
Connects via USB
TJ, EE

## Slide 33: Camera Selection: USB vs CSI Camera Main function: Object identification
Specs | CSI Camera | USB Camera
Connection | Camera Serial Interface | USB
Image Quality | Made specifically for Raspberry Pi, typically high | Moderate to high
Latency | Lower latency due to CSI connection | Higher latency because of USB overhead
Power Consumption | Low, powered directly from board | Depends on model
TJ, EE

## Slide 34: Raspberry Pi Camera V2.1 by Raspberry Pi Ltd.
8 megapixel Sony IMX219 image sensor
3280 x 2464 pixel static images
Supports 1080p30, 720p60, and 640x480p90 video
Provides enough quality for object detection
Interfaces directly with Raspberry Pi 4
TJ, EE

## Slide 35: Safety Shield Mechanism Selection: Linear actuator vs Motorized Pulley Main function: Lowers safety shielding before laser use
Specs | Linear Actuator | Motorized Pulley
Precision | High precision for positioning | Moderate precision, varies with tension
Speed | Typically slower | Can be faster with motor choice
Complexity | Compact and self-contained | More complex: needs motors, pulley, cables, etc
TJ, EE

## Slide 36: Linear Actuator
12v Volt-Electric Linear Motor Actuator
Quiet operation, waterproof, can move 220 lbs 0.47"/sec
Will lower the safety shutter made of 250nm to 520nm Laser Shielding obtained from J Tech Photonics, Inc.
Shielding is an optical grade semi-transparent acrylic material that has been tested with 405nm and 445nm lasers to show an OD of 3+
TJ, EE

## Slide 37: Software Comparison & Selection
ESP32 WROOM |  |  |  | 
 | PlatformIO | Arduino IDE | MicroPython | Notes
Language | Python | C++ | Python | C++ is faster than Python
Performance | High | Medium | Low | Depends on libraries used and the project
Experience Required | Advanced | Beginner | Beginner | PlatformIO is used for more complex embedded projects
ESP-IDF | Yes | No | Yes | It’s the official framework for the ESP32

## Slide 38: Raspberry Pi Object Detection

## Slide 39: MCU to PCB

## Slide 40: ESP32 Motor Control

## Slide 41: Laser Control System

## Slide 42: Laser Design Hardware
 | LEDs | Laser Diodes
Particle Phase | Incoherent | Coherent
Direction | Random | Linear
Output Power | 10 – 50 µW | 1 – 1000 mW
Rise Time | 1 to 100 ns | < 1 to 10 ns
Temperature Effects | Increases wavelength by .6 nm/ °C | Wavelength varies by .25 nm/ °C Threshold current rises by .5mA/ °C
Laser Diodes
Easy to achieve higher intensities
Have narrower beam

## Slide 43: Laser Design Hardware
 | Chlorophyll A | Chlorophyll B
Absorbed Light Wavelength | 430 – 660 nm | 450 – 650 nm
Absorption Peak | 430 nm & 662 nm | 470 nm
Absorbed Light | Violet-blue & Orange-red | Orange-red
Color Reflected | Blue-green | Yellow-green
Organism Types | all plants, algae, and cynobacteria | All plants and green algae
Proportion in Total Chlorophyll in Plants |  | 
 | Chlorophyll A | Chlorophyll B
Absorbed Light Wavelength | 430 – 660 nm | 450 – 650 nm
Absorption Peak | 430 nm & 662 nm | 470 nm
Absorbed Light | Violet-blue & Orange-red | Orange-red
Color Reflected | Blue-green | Yellow-green
Organism Types | all plants, algae, and cynobacteria | All plants and green algae
Proportion in Total Chlorophyll in Plants |  | 
Laser Color for Treatment : Blue & Red

## Slide 44: Laser Design Hardware
Laser Diode
Color | Wavelength | Power
Blue | 465 nm | 1-2 W
Red | 638 nm | 1-2 W
Lens
 | Type | Material | Wavelngth | Focal Length | Effective Focal Length | Dimension | Thickness
G8 | Aspheric | Glass | 400 – 700 nm | 7 mm | 8 mm | M9 X 0.5 | 2.3 mm

## Slide 45: Laser Design Hardware
Red Laser Diode
Model | ML562G85-02 | 665A-110-2-1.5-TO9
Output Power | 2100 mW | 2000 mW
Wavelength Range | 635 – 644 nm | 665 nm
Peak Wavelength, | 639 nm | 665 nm
Operation Current, | 2.25 A | 2.0 – 2.2 A
Operation Voltage, | 2.25 V | 2.4 V
Module Diameter | 9.0 mm | 9.0 mm TO9
Slope Efficiency, | 1.2 W/A | 1.3 W/A
Cost | $36.50 | $120.76
Model | ML562G85-02 | 665A-110-2-1.5-TO9
Output Power | 2100 mW | 2000 mW
Wavelength Range | 635 – 644 nm | 665 nm
 | 639 nm | 665 nm
 | 2.25 A | 2.0 – 2.2 A
 | 2.25 V | 2.4 V
Module Diameter | 9.0 mm | 9.0 mm TO9
 | 1.2 W/A | 1.3 W/A
Cost | $36.50 | $120.76

## Slide 46: Laser Design Hardware
Model | NUBM07E | M140-M
Output Power | 2900 mW | 2100 mW
Wavelength Range | 460 – 470 nm | 435 -455 nm
Peak Wavelength, | 465 nm | 445 nm
Operation Current, | 2.3 A | 1 - 1.7 A
Operation Voltage, | 3.7 – 5.5 V | 3.7 – 5.5 V
Module Diameter | 9 mm TO5 | 5.6 mm TO18
Slope Efficiency, | 1.6 W/A | 1.845 W/A
Cost | $50.83 | $10.95
Model | NUBM07E | M140-M
Output Power | 2900 mW | 2100 mW
Wavelength Range | 460 – 470 nm | 435 -455 nm
 | 465 nm | 445 nm
 | 2.3 A | 1 - 1.7 A
 | 3.7 – 5.5 V | 3.7 – 5.5 V
Module Diameter | 9 mm TO5 | 5.6 mm TO18
 | 1.6 W/A | 1.845 W/A
Cost | $50.83 | $10.95
Blue Laser Diode

## Slide 47: Laser Design Hardware
 | NUBM07E | M140-M
Parallel (°) | 0.55 | 14
Perpendicular (°) | 0.8 | 44
Maximum Beam Divergence

## Slide 48: Laser Design Hardware
Intensity
Power
Spot Size
Laser
Collimating Lens
Focus Lens
Plants
Treatment
Working Distnace > 1 cm
Duration 30-60 sec

## Slide 49: PCB Design

## Slide 50
PCB Flow Chart
TJ, EE

## Slide 51
Regulator Circuit
TJ, EE

## Slide 52
Features:
Terminal blocks for breadboard testing
GND planes for heat dissipation
M5 Mounting holes
TJ, EE

## Slide 53
TJ, EE

## Slide 54
TJ, EE

## Slide 55
TJ, EE

## Slide 56
TJ, EE

## Slide 57
Daemy, EE

## Slide 58
Daemy, EE

## Slide 59
Ryan, EE

## Slide 60
GND planes for heat dissipation
M5 Mounting holes
Silkscreen Layer and VIAs used for proper labeling and functionality
Ryan, EE

## Slide 61: Software Design
This system will be broken down into required components for readability
Ryan, EE

## Slide 62: Lidar
While the system is active, the Lidar is tasked with continually determining if and how much the robot has moved at any given time
The Lidar is then tasked with storing the location data, and instructing the motors to move if necessary
The Lidar uses the location data to continue to map out the area, using feedback loops to continuously iterate the process
Ryan, EE

## Slide 63: Software Design – Laser Control System
A camera feed from the Raspberry Pi will be constantly supplied to the ESP-32-WROOM
The ESP-32 will move the laser control system's stepper motors to the correct determined location of the weed
The robot will stop to adjust the laser, then which a shield enclosed laser module will lower to designated area and activate.
This process is ran continuously until there are no more weeds detectable by the raspberry pi
Ryan, EE

## Slide 64: Software Design – MCU
The MCU (Consisting of an ESP-32 and Raspberry Pi 4) is the middle man and bridge for the entirety of the robot's systems
The MCU is required to keep track of the battery, as well as the solar charging system to keep itself powered
The MCU is responsible for tracking storage and sensor data, as well as returning that info to the application
Ryan, EE

## Slide 65: Software Design – Stretch Goals
Ideally as a stretch goal we wanted to give the application much more attention.
The application would be able to not only monitor the robots current weeding process, but take remote control and or call back the robot if needed.
The application would be connected to an external server, allowing for fast and secure data uploading and integration after every session, giving the most accurate and helpful data in a way that is easy to understand
Ryan, EE

## Slide 66: Software Design
Ryan, EE

## Slide 67: Hardware & Software Testing
Our Hardware Testing comprised of us testing our various PCBs on breadboards as this was one of the fastest ways to confirm our intended functionality
We used the System On Chip (SOC) microcontrollers in order to properly test our designs, including ESP-32-WROOM
Our Software testing consists of us program our microcontrollers and motor circuits in order to test their proper functionality using the Arduino IDE
Ryan, EE

## Slide 68: Performance Evaluation
We take careful consideration in evaluating each of our parts are the correct choice for its purpose and that it will function as we intend it to
Our PCB designs were cleared by our advisors, so we are confident once everything is wired, tested, and revised for needed issues, the robot should perform as we intend
Additionally tests will be done to confirm the performance of the laser driver circuit and laser diode by our PSE member to ensure the proper functionality within the context of our goals and objectives
Ryan, EE

## Slide 69: Problems and proposed solutions
Problem | Solution
Issues with hardware while testing designs. | Continue testing and troubleshooting hardware to resolve issues.
Difficulty with software and coding due to lack of formal coding training and a dedicated coder, slowing progress. | Work diligently as a team to develop programs and use all available resources to improve software progress.
Ryan, EE

## Slide 70: Prototyping & Testing
Hardware & Software Testing
Performance Evaluation
Success
Difficulty, problem and proposed solution

## Slide 71: Administrative Content

## Slide 72: Budget
Item | Description | Total Cost
Hardware | Chassis, sensors, DC motors | $273
 | Solar Panel | $50
Laser Control System | Stepper motors and drivers, timing pulley | $100
Laser System | Diodes, Driver Board | $282
PCB | Boards, ICs, resistors, capacitors, etc | $160
Total |  | $865
Daemy, EE
Notes: Add manufacturer

## Slide 73: BOM
Daemy, EE
Item | Quantity | Price
Peripherals |  | 
Raspberry Pi B | 1 | 65.76
Pi Camera Module V2 | 1 | 14.99
Lidar | 1 | 100
Linear Actuator 5.9'' | 1 | 26.99
 | Total | $207.74
PCB |  | 
BTS7960B | 15 | 20.31
JLCPCB | 25 | 40.39
Digikey | 1 | 227.38
 | Total | $288.08
Laser System |  | 
Board Driver | 3 | 76.62
Diode Housing | 2 | $29.70
Diode | 2 | 23.93
Blue Diode | 5 | 146.9
Red Diode | 2 | 100.92
 | Total | $378.07
Laser Control System |  | 
Cable Wrap | 2 | 11.98
Pulley & Belt | 15 | 27.93
Gantry | 2 | 18.22
Stepper Motor | 2 | 35.96
 | Total | $94.09
Frame |  | 
Rail | 19 | 37.66
Screws & nuts | 4 | 80.43
Mounting Plate | 2 | 6.46
 | Total | $124.55
Hardware |  | 
DC Motor Transmission | 4 | 57.32
Wheels | 4 | 25.55
Chargers | 2 | 67.81
Shipping |  | 30.7
Solar Panel | 1 | 45
Battery | 1 | 91.05
Board Driver | 1 | 8.99
Cables | 2 | 20
Fuses | 1 | 5
Fuse Holder | 1 | 5.31
 | Total | $356.73
Item | Quantity | Price
Total
$1449.26
Notes: Add manufacturer

## Slide 74: Work Distribution
Student | Main Tasks | Secondary Tasks
TJ Jones | Stepper Motor Driver Schematic and PCB Design | MCU Schematic and PCB Design
TJ Jones | Switching Regulator Schematic and PCB Design | 
Suhyun Hwang | Lens and Laser Diodes Research, and Selection | Laser System Implementation
Suhyun Hwang | Laser System Research, selection, Design | 
Ryan Takiff | Lidar Sensor Selection, and Implementation | SLAM Localization
Ryan Takiff | MCU Schematic and PCB Design | 
Daemy Luzardo | Navigation System Implementation | Object Detection Data Set
Daemy Luzardo | DC Motor Driver Schematic and PCB Design | 
Daemy, EE

## Slide 75: Progress & Plan for Completion
Fixing: Ordering more parts / reassembling when error detected after the final demo
Present
Frame & PCB Assembly / Testing
PCB Design Finalization / Parts figured out
Software/
Laser Testing
Testing / Fixing
Final Demo
Suhyun

## Slide 76: Thank You